| Last Modified: 06-07-2019 | 6.8:8.0.48 | Doc ID: RM100000000Q458 |
| --- | --- | --- |
| Model Year Start: 2016 | Model: ES350 | Prod Date Range: [07/2015 - ] |
| Title: 2GR-FE FUEL: FUEL PUMP: REMOVAL; 2016 - 2018 MY ES350 [07/2015 - ] |

## REMOVAL

## CAUTION / NOTICE / HINT

HINT:

- If a malfunction such as pump lock occurs and the fuel pump is damaged, excessive current may be continuously applied to the fuel pump control ECU assembly, damaging its internal parts. Make sure to replace the fuel pump control ECU assembly at the same time when replacing the fuel pump with filter assembly.

- Perform "Inspection After Repair" after replacing the fuel pump with filter assembly (See page ).

## PROCEDURE

1. PRECAUTION

NOTICE:

After turning the engine switch off, waiting time may be required before disconnecting the cable from the negative (-) battery terminal. Therefore, make sure to read the disconnecting the cable from the negative (-) battery terminal notice before proceeding with work (See page ).

2. DISCHARGE FUEL SYSTEM PRESSURE

(See page )

3. DISCONNECT CABLE FROM NEGATIVE BATTERY TERMINAL

NOTICE:

When disconnecting the cable, some systems need to be initialized after the cable is reconnected (See page ).

4. REMOVE REAR SEAT CUSHION ASSEMBLY

5. REMOVE REAR FLOOR SERVICE HOLE COVER

| (a) Remove the rear floor service hole cover. |  |
| --- | --- |

(b) Disconnect the fuel pump connector.

6. DISCONNECT FUEL TANK VENT HOSE SUB-ASSEMBLY

| (a) Pull the retainer to disengage the lock claws and pull out the fuel tank vent hose sub-assembly. Text in Illustration *1 Retainer NOTICE: Remove any dirt or foreign matter on the fuel tank vent hose connector before performing this work. Do not allow any scratches or foreign matter on the parts when disconnecting them as the fuel tank vent hose connector has an O-ring that seals the pipe. Only disconnect the joint by hand. Do not forcibly bend, twist or turn the fuel tank vent hose sub-assembly. Protect the disconnected part by covering it with a plastic bag after disconnecting the fuel tank vent hose sub-assembly. If the fuel tank vent hose connector and pipe are stuck, push and pull to release them. |  |
| --- | --- |

7. DISCONNECT FUEL TANK BREATHER TUBE SUB-ASSEMBLY

| (a) Remove the tube joint clip, and pull out the fuel tube joint of the fuel tank breather tube sub-assembly. Text in Illustration *1 Tube Joint Clip *2 Fuel Tube Joint *3 Fuel Tank Breather Tube Sub-assembly *4 O-ring *5 Fuel Suction Plate Sub-assembly NOTICE: Remove any dirt or foreign matter on the fuel tube joint before performing this work. Do not allow any scratches or foreign matter to get on the parts when disconnecting them as the fuel tube joint has an O-ring that seals the pipe. Only disconnect the fuel tube joint by hand. Do not forcibly bend, twist or turn the fuel tank breather tube sub-assembly. Protect the disconnected part by covering it with a plastic bag after disconnecting the fuel tube joint. If the fuel tube joint and fuel suction plate sub-assembly are stuck, push and pull to release them. |  |
| --- | --- |

8. DISCONNECT FUEL TANK MAIN TUBE SUB-ASSEMBLY

| (a) Remove the tube joint clip, and pull out the fuel tube joint of the fuel tank main tube sub-assembly. Text in Illustration *1 Tube Joint Clip *2 Fuel Tube Joint *3 Fuel Tank Main Tube Sub-assembly *4 O-ring *5 Fuel Suction Plate Sub-assembly NOTICE: Remove any dirt or foreign matter on the fuel tube joint before performing this work. Do not allow any scratches or foreign matter to get on the parts when disconnecting them as the fuel tube joint has an O-ring that seals the pipe. Only disconnect the fuel tube joint by hand. Do not forcibly bend, twist or turn the fuel tank main tube sub-assembly. Protect the disconnected part by covering it with a plastic bag after disconnecting the fuel tube joint. If the fuel tube joint and fuel suction plate sub-assembly are stuck, push and pull to release them. |  |
| --- | --- |

9. REMOVE FUEL TANK VENT TUBE SET PLATE

| (a) Remove the 8 bolts and fuel tank vent tube set plate. |  |
| --- | --- |

10. REMOVE FUEL SUCTION TUBE WITH PUMP AND GAUGE ASSEMBLY

| (a) Using a screwdriver with its tip wrapped in protective tape, pull the retainer to disengage the lock claws and pull out the fuel cut-off tube. Text in Illustration *1 Retainer *2 Fuel Cut-off Tube *3 Fuel Suction Tube Set Gasket |  |
| --- | --- |

(b) Remove the fuel suction tube with pump and gauge assembly from the fuel tank sub-assembly.

NOTICE:

Make sure that the fuel sender gauge arm does not bend.

(c) Remove the fuel suction tube set gasket from the fuel suction tube with pump and gauge assembly.