How to DIY (Clunk Greasing) for out of Warranty GX Owners for Shaft Clunk/Thump Noise

Introduction:- This method is for owners who suffer from Shaft Clunk /thump Noise on the GX Models , who do not have Warranty covered any more.

Job Area – Shaft Assembly / Propeller Front & Rear Axles

Tools Required :

1. Lever Operated Grease Gun – Pistol Type ( Brand Used Snap On tool )

Type GA471 – 3 oz Capacity / 8 1/4 nozzle  . Cost 30/$

2. Grease – Molybdenum sulphide – Lithium Based ( 500gm) Tin

Repair Procedure:-

- Vehicle needs to be jacked ( ensure the height control s/w is “OFF” mode and appropriate height for easy access to the Propeller Shaft Assy. Rotate the wheel so that shaft placing the Grease Gun is visible. Different Terms are used for the same Location ( U-Joint / Spider Joint / Drive Shaft ).

- On the Shaft Assy between the yoke and Flange you will notice Greasing fitting. Lock  the grease gun on the Grease fitting & once the MB Sulphide grease is pre-loaded and have it lubricated until the old grease is pumped out between the flange seals. There are Two Grease Nipple pins at each yoke/Flange point.

- The Grease points are at the Rear Propeller Assy Flange both Front and Rear Yoke.

(L) Image – Rear Propeller Yoke / Flange View( Above)   (R) Image – Front Propeller Yoke / Flange View (Above)

4. Once they are completed, Ensure to Re-torque( 48 Ft,lbs)  the Drive Shaft Flange Bolts and then lower the vehicle and start the vehicle & ensure to push the Height Rise s/w to “ON” position.

Now go for a test ride, you will notice the difference in ride.

5.  You could have a Vehicle Body Under Wash done so that the old grease which has been spurted while driving on the under chassis is completely removed off.