## REMOVAL

## PROCEDURE

1. REMOVE REAR SPOILER SUB-ASSEMBLY

Click here

2. REMOVE CENTER STOP LIGHT ASSEMBLY

(a) Apply protective tape to the area shown in the illustration.

|  | Protective Tape |
| --- | --- |

| (b) Remove the 2 screws. |  |
| --- | --- |

| (c) Using a moulding remover, disengage the claw and 2 guides as shown in the illustration. |  |
| --- | --- |

| (d) Disconnect the connector to remove the center stop light assembly. |  |
| --- | --- |